Zigbee Explorer
Technical Functional Specification
DRAFT

Author: Andrea Ravalli
Date: 08/03/2017
Revision: 0.5.1

Table of Contents

Table of Figures
# Document Purpose

This document purpose is to support engineers developing appliance compliant with the Zigbee Home Automation 1.2 profile using Digi’s Xbee S2C radio module and an external controller connected via serial port.
This document describes how to use Xbee serial API to send to implement the Zigbee application layer.
# Zigbee protocol stack

Below are reportet two figures depiting the Zigbee protocol stack organization with reference to the OSI model and to the offered services.

Figure 1: This figure shows which building block is responsible for the implementation of each Zigbee protocol stack element.

Figure 2: In this figure are highlighted the offered services for each Zigbee protocol stack element.

# Definitions

Below are reported the definitions used in this document.
## Addresses

- 64bit address BROADCAST:
  0x000000000000FFFF
- 16bit address UNKNOWN (BROADCAST):
  0xFFFE
- DEV_ADDR_64: 64 bit address for a known device (already added to the associated device map):
  0xXXXXXXXXXXXXXXXX
- DEV_ADDR_16: 16 bit address for a known device (already added to the associated device map):
0xYYYY
## Other definitions

Unspecified values or to be calculated are marked by dashes:
1 byte to be calculated ‘0x—‘

## Frame Types
### TX_EXPLICIT

Il Explicit Addressing Command frame sarà indicato brevemente come tx_explicit.
Esso permette di inviare frame di comando esplicitantando anche gli indirizzi di destinazione. Richiede API Output (AO) mode settato ad 1 o superiore.
Per dettagli vedere pag 161 di Xbee_S2C_manual_90002002.pdf.

### RX_EXPLICIT

Il Explicit Rx Indicator frame sarà indicato brevemente come rx_explicit.
Rappresenta la risposta ad un frame di comando di tipo tx_explicit con AO>=1.
Per dettagli vedere pag 176 di Xbee_S2C_manual_90002002.pdf

# Xbee module configuration

## Settings

Zigbee Coordinator	(CE)	1
Device Join Permit	(JN)	FF
Zigbee Stack Profile	(ZS)	2
Encryption Enable	(EE)	1
Encryption Options	(EO)	0
Encryption Key	(KY)	5a6967426565416c6c69616e63653039
Network Encryption Key	(NK)	0
API Enable	(AP)	1
API Output Mode	(AO)	3
Sleep Mode	(SM)	1

## AT command sequence

Below is reported the list of AT commands as they were sent to the XBee device in “transparent mode”, ordered such to avoid command conflicts/device inconsistent states. The same commands can be sent in “API mode” using the “AT command frame”
The string ‘ERROR’ is reported on the serial output in case of write failures.
The string ‘OK’ is reported …
+++
ATSM 1
ATCE 1
ATJN FF
ATZS 2
ATEE 1
ATEO 0
ATKY 5a6967426565416c6c69616e63653039
ATNK 0
ATAP 1
ATAO 3
ATWR
ATFR

# General Concepts

## Xbee explicit frames and APS frames

The Xbee firmware will abstract all the Zigbee protocol levels up to the APS level.

Figure 3: Zigbee stack in detail.
APS frames payload is encapsulated inside the Xbee explicit frame in the “payload” field. This field is sent as is over the air and since that has to written in “little endian” byte order.

Figure 4: Zigbee stack with frames envelopment.
## Reading ZDO message

In order to read ZDO messages the Xbee AO (API Output mode) needs to be set to 3.
ZDO messages needs to be formatted as APS frames including the APS header (frame type and transaction id included). Detail about the APS frames can be found in ZigbeeSpec  cap 2.4.2.8.
# Nodes and Service Discovery

This chapter will list all ZDO frames useful to the construction of the coordinator’s map of all the devices belonging to his network altogether with the services they offer.

## Route Record Request

- Cluster ID: 0x0032
- Profile ID: 0x0000

### Description

Il coordinator al suo avvio controlla quali dispositivi appartengono alla sua rete chiedendo i il contenuto della loro routing table ai dispositivi connessi.
Questa azione può (deve?) essere usata per costrure la tabella dei dispositivi connessi.
Details are available at page 12 of APP_NOTE_XBee_ZigBee_Device_Profile.pdf

### Pseudo code

zb.send('tx_explicit',
dest_addr_long = BROADCAST,
dest_addr = UNKNOWN,
src_endpoint = '\x00',
dest_endpoint = '\x00',
cluster = '\x00\x32',
profile = '\x00\x00',
data = '\x12'+'\x01'
)

### Frame

Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x0015
Frame Type	3	0x11
Frame Seq ID	4	0xAA
64-bit dest addr	MSB 5 - LSB 12	BROADCAST
16-bit dest addr	MSB 13 - LSB 14	UNKNOWN
src end point	15	0x00
dest end point	16	0x00
cluster ID	17-18	0x0032
Profile ID	19-20	0x0000
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	23-24	0x12 0x01
Checksum	25	--

Payload Data description
data fields	Offset	Example
Transaction ID	0	0x12
Start Index	1	0x01

Hexadecimal representation:
0x76001511AA000000000000FFFFFFFE00000032000000001201--

## Route Record Response

- Cluster ID: 0x8032
- Profile ID: 0x0000

### Description

This message is the reply to a Route Record Request and his payload will report the routing table of the answering device if supported, otherwise a CLUSTER_UNSUPP error code will returned.
Since this message can be received multiple times (if the request was sent in broadcast) even from device not supporting this cluster (typically ZED does not support it), it can be used as alternate strategy for discovering all nodes joined to a network (only the awaken devices will reply).
Details are available at page 12 of APP_NOTE_XBee_ZigBee_Device_Profile.pdf
### Pseudo code
N/A.
### Frame

Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x91
64-bit dest addr	MSB 4 - LSB 11	DEV_ADDR_64
16-bit dest addr	MSB 12 - LSB 13	DEV_ADDR_16
src end point	14	0x00
dest end point	15	0x00
cluster ID	16-17	0x8032
Profile ID	18-19	0x0000
rx options	20	0x--
Data Payload	21-n	--
Checksum	n+1	--

Data Payload description:
data fields	Offset	Example
Transaction ID	0	0x12
Routing Table	1	0x01

Routing Table:
Field Name	Size (bytes)	Description
Routing Table Entries	1
Routing Table Entries	1	The total number of routing table entries
Start Index	1	The starting point in the routing table
Routing Table List Count	1	The number of routing table entries in this response
Routing Table List	Variable	A list of routing table entries.

For the Routing Table List details see p.12 di APP_NOTE_XBee_ZigBee_Device_Profile.pdf.
Hexadecimal representation: N/A

## Active Endpoint Request

- Cluster ID: 0x0005
- Profile ID: 0x0000

### Description

Transmission used to discover the active endpoints on a device with a matching 16-bit address.
This action is part of the service discovery process.
Details are available at page 7 of APP_NOTE_XBee_ZigBee_Device_Profile.pdf

### Pseudo code

zb.send('tx_explicit',
dest_addr_long = DEV_ADDR_64,
dest_addr = DEV_ADDR_16,
src_endpoint = '\x00',
dest_endpoint = '\x00',
cluster = '\x00\x05',
profile = '\x00\x00',
data = DEV_ADDR_16 [1]+ DEV_ADDR_16 [0]
)

### Frame

Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x0015
Frame Type	3	0x11
Frame Seq ID	4	0x--
64-bit dest addr	MSB 5 - LSB 12	DEV_ADDR_64
16-bit dest addr	MSB 13 - LSB 14	DEV_ADDR_16
src end point	15	0x00
dest end point	16	0x00
cluster ID	17-18	0x0005
Profile ID	19-20	0x0000
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	MSB 23 - LSB 24	DEV_ADDR_16
Checksum	25	--

Payload Data description
data fields	Offset	Example
Transaction ID	0	0x12
Device addres	1	DEV_ADDR_16

Hexadecimal representation:
0x76001511-- XXXXXXXXXXXXXXXXYYYY0000000500000000YYYY--

## Active Endpoint Response

- Cluster ID: 0x8005
- Profile ID: 0x0000

### Description

Reports the list of active endpoints supported on the device and shall be stored as node attribute.
Details are available at APP_NOTE_XBee_ZigBee_Device_Profile.pdf page 7.
### Pseudo code
N/A.
### Frame

Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x91
64-bit dest addr	MSB 4 - LSB 11	DEV_ADDR_64
16-bit dest addr	MSB 12 - LSB 13	DEV_ADDR_16
src end point	14	0x00
dest end point	15	0x00
cluster ID	16-17	0x8005
Profile ID	18-19	0x0000
rx options	20	0x--
Data Payload	21-n	--
Checksum	n+1	--

Data Payload description
data fields	Offset	Example
Transaction ID	0	0x12
Active End points	1	--

Active End points list:
Field Name	Size (bytes)	Description
Status	1
Network Address	2	Indicates the 16-bit address of the responding device
Active Endpoint Count	1	Number of endpoints in the following endpoint list
Active Endpoint List	n	List of endpoints supported on the destination device. One byte per

Data payload description extracted from APP_NOTE_XBee_ZigBee_Device_Profile.pdf p.7.
Hexadecimal representation: N/A

## Simple Descriptor Request

- Cluster ID: 0x0004
- Profile ID: 0x0000

### Description

Once that the end points are mapped to the device this ZDO command shall be used to discover the their capabilities.
Details are available at APP_NOTE_XBee_ZigBee_Device_Profile.pdf page 6.
### Pseudo code

zb.send('tx_explicit',
dest_addr_long = data['source_addr_long'],
dest_addr = data['source_addr'],
src_endpoint = '\x00',
dest_endpoint = '\x00',
cluster = '\x00\x04',
profile = '\x00\x00',
data = '\x13' + data['source_addr'][1] + data['source_addr'][0] + '\x01'
)

### Frame

Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x0016
Frame Type	3	0x11
Frame Seq ID	4	0x--
64-bit dest addr	MSB 5 - LSB 12	DEV_ADDR_64
16-bit dest addr	MSB 13 - LSB 14	DEV_ADDR_16
src end point	15	0x00
dest end point	16	0x00
cluster ID	17-18	0x0004
Profile ID	19-20	0x0000
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	23-25	YYYY01
Checksum	26	--

Payload Data description
data fields	Offset	Example
Transaction ID	0	--
Device addres	1	DEV_ADDR_16
Target End Point	3	0x1

Hexadecimal representation:
0x76001511--XXXXXXXXXXXXXXXXYYYY0000000400000000YYYY01--

## Simple Descriptor Response

- Cluster ID: 0x8004
- Profile ID: 0x0000

### Description

This message will report the simple descriptor of the device. This descriptor contenis all the useful details related to the queried end point, included the device ID, defining the device class and purpose, and the available clusters on it.
Details are available at page 6 of APP_NOTE_XBee_ZigBee_Device_Profile.pdf
### Pseudo code
N/A.
### Frame

Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x91
64-bit dest addr	MSB 4 - LSB 11	DEV_ADDR_64
16-bit dest addr	MSB 12 - LSB 13	DEV_ADDR_16
src end point	14	0x00
dest end point	15	0x01
cluster ID	16-17	0x8005
Profile ID	18-19	0x0000
rx options	20	0x--
Data Payload	21-n	--
Checksum	n+1	--

Data Payload description
data fields	Offset	Example
Transaction ID	0	0x12
Descriptor	1	--

Descriptor:
Field Name	Size (bytes)	Description
Status	1
Network Address	2	Indicates the 16-bit address of the responding device
Length	1	Length of the simple descriptor
Simple Descriptor	Variable	See simple descriptor below.

Name	Size (bits)	Description
Endpoint	8	The endpoint on the node to which this descriptor refers.
Application profile ID	16	The profile ID supported on this endpoint.
Application device ID	16	Specifies the device description identifier supported on the device
Application device version	4	The version of the device description supported on this endpoint.
Reserved	4
Input cluster count	8	The number of input clusters supported on this endpoint.
Input cluster list	Variable	The list of input clusters supported on this endpoint. Each cluster is 2 bytes in size. This field is not included if the input cluster count is 0.
Output cluster count	8	The number of output clusters supported on this endpoint.
Output cluster list	Variable	The list of output clusters supported on this endpoint. Each cluster is 2 bytes in size. This field is not included if the output cluster count is 0.

Data payload description extracted from APP_NOTE_XBee_ZigBee_Device_Profile.pdf p.6.
Hexadecimal representation: N/A

## Device Announce Message

- Cluster ID: 0x0013
- Profile ID: 0x0000

### Description

Sent by devices announcing them self in the network.
This devices need to be added to the associated device map.

### Pseudo code
N/A.
### Frame

Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x91
64-bit dest addr	MSB 4 - LSB 11	DEV_ADDR_64
16-bit dest addr	MSB 12 - LSB 13	DEV_ADDR_16
src end point	14	0x00
dest end point	15	0x00
cluster ID	16-17	0x0013
Profile ID	18-19	0x0000
rx options	20	0x--
Data Payload	21	--
Checksum	n+1	--

Data Payload description
Field Name	Size (bytes)	Description
Transaction ID	1
Capabilities	1

Hexadecimal representation: N/A

# Nodes discovery: startup sequence and persistency

At boot time the device should load from the Xbee persistency the list of associated devices. These data are stored by Xbee module in its persistency and can be retrieved by requesting the neighbor table (ZDO cluster 0x0032) or the child table (extended request for ZDO cluster 0x0000 and 0x0001).
The information retrieved should be stored in a set of suitable data structure or in a DB.
## Psedocode

if starting
send: neighbor_table_req(coordinator)
while: running
if new_message
goto: parse_msg
print: dev_map
parse_msg:
if neighbor_table_res or device_announce:
add discovered_device to device_map
for each dev in device_map do:
send: active_endpoint_req
else if active_end_point_res:
build end_point_map
link end_point_map to device_entry in device_map
for each end_point in end_point_map do:
send: simple_descriptor_req
else if simple_descriptor_re:
add: descriptor to end_point in end_point_map

## Sequence Diagram
TBD

## Data Types (proposal)

# Intruder Alarm System Devices

On a Zigbee network a special regards is dedicated to the security devoted devices and are managed under the IAS, Intrusion and Alarm System, set.
The IAS devices are classified in: Control Indicating Equipment (CIE), Zones device, Warning Device (WD) and Ancillary Control Equipment (ACE).
CIE devices are in charge to collect all the alarms coming from Zone devices and they will implements all the related business logic. For instance, in case it’s available in the network, it will activate the WD device.
Others details about the IAS device family (and related clusters) are available in chapter 8 of ZCL.
We will take care only of the CIE and Zones device: the CIE is our network coordinator and the Zones devices are the managed sensors. They are described in chapter 8 of the ZCL and in chapters 7 and 10.7 through 10.9.
The Home Automation profile extends the ZCL definition IAS cluster’s attributes and commands.

## Enrolment Sequence

An IAS Zone device joining a new network needs to know who is the CIE for that network and in case there is more than just one, which one is controlling his zone. In other term it needs to know to whom has to send its alarms.
This task is split in two parts: the service discovery and the enrollment sequence.
### Service discovery
The service discovery is initiated by the IAS Zone devices immediately after joining a network by sending a Matching_Desc_req message and waiting for a response.
The request is sent in broadcast and is repeated for a few times in intervals of a few seconds (for the Heinman Water Leakage sensor it’s repeated 11 times in intervals of 9 seconds).
If a successful Matching_Desc_res is received the IAS Zone device will start the enrollment sequence described in the next chapter.
If after the max number of attempts the IAS Zone will not receive a Matching_Desc_res it will enter in an “idle” state waiting for commands.
That is the case when the CIE device is joining the network after the Zone device.
In this case the CIE will perform a service discovery by using the ZDO commands described in 4.5 and once it found an IAS Zone device (device ID 0x0402), it can trigger the enrollment sequence by explicitly writing its IEEE address in the IAS_CIE_Address attribute of the Zone device.
### Enrollment sequence

With the enrolment sequence the Zone device require the CIE to take in charge its zone. If the CIE addressed by the request (more than one CIE is possible in the network) has interest for the requiring Zone (there are several reason for a CIE to discard a Zone) will it a zone (will beaded to a zone in the zones table) and then send a success message with the assigned zone id.
Below are reported the sequence for the enrollment in the two scenarios where, first, the initiator is the Zone device and, second, the initiator is the CIE.

IAS CIE Device
IAS Zone Device

The device has join the network
Device Announce
Matching_Desc_req
Matching_Desc_res
Zone_Enroll_req
Zone_Enroll_res

Figure 5: Enrollment sequence triggered the Zone device after joining the network. In this scenario the initiator is the Zone device searching (Matching_Desc_req) for a CIE device in the network.

IAS CIE Device
IAS Zone Device

The device has just discovered an IAS Zone devive in the network
write: IAS_CIE_Address
write success
Zone_Enroll_req
Zone_Enroll_res
Figure 6: Enrollment sequence triggered by the CIE writing the IAS_CIE_Address attribute of the Zone device. In this scenario the initiator is the CIE discovering a new Zone device in the network.

## Commands and attributes

Cleared that the “server” role is kept for the device owning the cluster attributes, for the IAS Zone cluster (0x0500) the server is the Zone device (ZED) and the client is the CIE (coordinator or router).
IAS Zone cluster’s attributes are split in attribute sets based on the value of 3 least significant nibbles of the attribute id (that is 2 bytes long).
Only two attribute set are defined in ZCL:
- Zone Information (read only): 0x000
- Zone Settings (read & write): 0x001
The next chapters will describe all the attributes and commands mentioned in 8.1.2. Additional details can be found at chapter 8.2 of ZCL.

### Enroll Request

This is a server side unicast request. The XBee module will present it as an “RX_EXPLICIT”.
Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x91
Frame Seq ID	4	0x--
64-bit dest addr	MSB 5 - LSB 12	CIE_ADDR_64
16-bit dest addr	MSB 13 - LSB 14	CIE_ADDR_16
src end point	15	0x01
dest end point	16	0xXX
cluster ID	17-18	0x0500
Profile ID	19-20	0x0104
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	23-25	YYYY
Checksum	26	--

Data Payload description:
Field Name	Size (bytes)	Description
Transaction ID	1

### Enroll Response

This is a client side unicast response. It will be sent through the XBee module as a “TX_EXPLICIT”.
Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x11
Frame Seq ID	4	0x--
64-bit dest addr	MSB 5 - LSB 12	DEV_ADDR_64
16-bit dest addr	MSB 13 - LSB 14	DEV_ADDR_16
src end point	15	0x01
dest end point	16	0xXX
cluster ID	17-18	0x0500
Profile ID	19-20	0x0104
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	23-27	--
Checksum	28	--

Data Payload description:
Field Name	Size (bytes)	Description
Frame Type	1
Transaction ID	1
Command	1
Enrolment Status	1
Zone ID	1

### Zone Status Change

This is a server side unicast notification. The XBee module will present it as an “RX_EXPLICIT”.
Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x91
Frame Seq ID	4	0x--
64-bit dest addr	MSB 5 - LSB 12	DEV_ADDR_64
16-bit dest addr	MSB 13 - LSB 14	DEV_ADDR_16
src end point	15	0x01
dest end point	16	0xXX
cluster ID	17-18	0x0500
Profile ID	19-20	0x0104
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	23-28	--
Checksum	29	--

Data Payload description:
Field Name	Size (bytes)	Value	Description
Frame Type	1	0b00000001
Transaction ID	1	0x--
Command	1
Zone Status	2		See 8.2.5
Zone Extended Info	1	0x0000	Reserved, shall be set to 0x0

### IAS_CIE_Address attribute

The server side attribute IAS_CIE_Address is part of the “Zone Settings” attributes set and stores the current CIE 64 bits address.
This attribute:
- has ID 0x0010 and type IEEE address (8 bytes byte array)
- is updated by the sever (the IAS Zone device) on positive Match_Desc_res or explicitly by the client using a normal “Write Attribute” command (see 9.2.1)
- when changed, will trigger the enrollment process (see 8.1.2)

### Zone Status attribute

The server side attribute Zone Status is part of the “Zone Information” attributes set and stores the current alarms status.
This attribute:
- has ID 0x0002 and type 16-bit bitmap
- each bit is set (1) by the corresponding alarm condition presence and reset (0) otherwise.
- First four bits represent, respectively: alarm1 and alarm2 (zone specific), tampering, battery level low. Please check ZCL chapter 8.2.2.2.1.3 for details.
### Zone State attribute

The server side attribute ZoneState is part of the “Zone Information” attributes set and stores the current enrolment status.
This attribute:
- has ID 0x0000 and type 8-bit enumeration.
- as for ZCL, may have only value “not enrolled” (0x00) and “enrolled” (0x01)
- is set on positive Enroll Response.

# Generic devices

In this chapter will be described operations not strictly related to a specific device type that are relevant for a consistent usage experience/service implementation.
These operation mostly rely on the commands defined in the Basic Cluster (ZCL chapter 3.2).
When using the commands defined in the Basic Cluster the frame type must be set as “profile wide” (mask 0b-------0).
## Device Binding and Attribute Reporting

## Attribute Reading and Writing

When a device is awake it’s possible to inquire its status or configuration by issuing an attribute read command. At the same way, writable attributes can be modified with a write attribute command. Both commands and the related response, are part of the ZCL Basic Cluster (clusters id 0x0000).
### Write attribute

This is a server side unicast command. It will be sent through the XBee module as a “TX_EXPLICIT”.
Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x11
Frame Seq ID	4	0x--
64-bit dest addr	MSB 5 - LSB 12	DEST_64
16-bit dest addr	MSB 13 - LSB 14	DEST_16
src end point	15	0x01
dest end point	16	0x01*
cluster ID	17-18	0x0500*
Profile ID	19-20	0x0104
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	23-25	YYYY
Checksum	26	--

*The and point and cluster ID depends on the attribute you want to write. Here, as example, is used the “IAS Zone” cluster on end point 1.

Data Payload description:
Field Name	Size (bytes)	Value	Description
Frame Type	1	0x00000001	Profile wide frame type w/o default response
Transaction ID	1	0x--	Example
Command ID	1	0x02	Write Attribute command ID
Attribute ID	2	0x0010	e.g. CIE Address
Attr. Data Type	1	0xF0	e.g. IEEE Address data type

### Write attribute response

This is a server side unicast response to a Write Attribute command. It will be sent through the XBee module as a “TX_EXPLICIT”.
Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x11
Frame Seq ID	4	0x--
64-bit dest addr	MSB 5 - LSB 12	DEST_64
16-bit dest addr	MSB 13 - LSB 14	DEST_16
src end point	15	0x01
dest end point	16	0xXX
cluster ID	17-18	0x0500*
Profile ID	19-20	0x0104
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	23-25	YYYY
Checksum	26	--

*The cluster ID depends on the attribute you want to write. Here, as example, is used the “IAS Zone” cluster.
Data Payload description:
Field Name	Size (bytes)	Value	Description
Frame Type	1	0x00000001	Profile wide frame type w/o default response
Transaction ID	1	0x--	Example
Command ID	1	0x02	Write Attribute command ID
Attribute ID	2	0x0010	e.g. CIE Address
Attr. Data Type	1	0xF0	e.g. IEEE Address data type

### Read attribute
This is a server side unicast command. It will be sent through the XBee module as a “TX_EXPLICIT”.
Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x11
Frame Seq ID	4	0x--
64-bit dest addr	MSB 5 - LSB 12	DEST_64
16-bit dest addr	MSB 13 - LSB 14	DEST_16
src end point	15	0x01
dest end point	16	0xXX
cluster ID	17-18	0x0500*
Profile ID	19-20	0x0104
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	23-25	YYYY
Checksum	26	--

*The cluster ID depends on the attribute you want to write. Here, as example, is used the “IAS Zone” cluster.
Data Payload description:
Field Name	Size (bytes)	Value	Description
Frame Type	1	0x00000001	Profile wide frame type w/o default response
Transaction ID	1	0x--	Example
Command ID	1	0x02	Write Attribute command ID
Attribute ID	2	0x0010	e.g. CIE Address
Attr. Data Type	1	0xF0	e.g. IEEE Address data type

### Read attribute response

This is a server side unicast command. It will be sent through the XBee module as a “TX_EXPLICIT”.
Frame details:
Frame data fields	Offset	Value
Start delimiter	0	0x7e
Length	MSB 1 - LSB 2	0x00--
Frame Type	3	0x11
Frame Seq ID	4	0x--
64-bit dest addr	MSB 5 - LSB 12	DEST_64
16-bit dest addr	MSB 13 - LSB 14	DEST_16
src end point	15	0x01
dest end point	16	0xXX
cluster ID	17-18	0x0500*
Profile ID	19-20	0x0104
broadcast radius	21	0x00
tx options	22	0x00
Data Payload	23-25	YYYY
Checksum	26	--

*The cluster ID depends on the attribute you want to write. Here, as example, is used the “IAS Zone” cluster.
Data Payload description:
Field Name	Size (bytes)	Value	Description
Frame Type	1	0x00000001	Profile wide frame type w/o default response
Transaction ID	1	0x--	Example
Command ID	1	0x02	Write Attribute command ID
Attribute ID	2	0x0010	e.g. CIE Address
Attr. Data Type	1	0xF0	e.g. IEEE Address data type

# History of changes

Version	Date	Description of change
Draft 0.1		Initial document
Draft 0.2		New document structure
Draft 0.3	12/12/2016	Enrollment sequence chapter and protocol stack diagrams added.
Draft 0.4	27/02/2017	Document moved to .odt format. Final document structure.
Draft 0.5	28/02/2017	Chapter 7.2 complete, Chapter 8 open.
Draft 0.5.1	08/03/2017	Draft 0.5 review